## Slide 1: Digital System Design Final Project
第六組
電機三 黃文璁
電機三 許耀中
電機三 陳博彥

## Slide 2: Outline
Architecture
  Jump instructions
  Branch
  Forwarding
  Stall
  Cache
  Critical path optimization
Extension
  Branch Prediction
  L2 Cache
  Multiplier, Divider
Experiments

## Slide 3: Architecture

## Slide 4: Jump Instructions
Handle jump instructions (J,JR,JAL,JALR) in ID stage
  Pros: only 1 bubbled cycle needed
  Cons: longer critical path

## Slide 5: Jump Instructions
Details
  J: can be done in IF, but handle in ID for convenience
  JR/JALR: need correct values of regs, forwarding is needed
  JAL/JALR: need additional controls LinkRA and LinkRD

## Slide 6
Jump datapath

## Slide 7: Branch
Handle BEQ in ID stage (baseline)
  Also need to use forwarded busX and busY
  In BrPred, we have to handle BEQ in IF and ID

## Slide 8
Branching (no BrPred)

## Slide 9: Forwarding
Forward to ID
  Similar to textbook, with additional ForwardEX conditions
  ForwardEX_X = EX_RegWrite & (EX_RW!=0) & (EX_RW==ID_RX);
  ForwardEX_Y = EX_RegWrite & (EX_RW!=0) & (EX_RW==ID_RY);
  ForwardMEM_X = MEM_RegWrite & (MEM_RW!=0) & (MEM_RW==ID_RX);
  ForwardMEM_Y = MEM_RegWrite & (MEM_RW!=0) & (MEM_RW==ID_RY);
  ForwardWB_X = WB_RegWrite & (WB_RW!=0) & (WB_RW==ID_RX);
  ForwardWB_Y = WB_RegWrite & (WB_RW!=0) & (WB_RW==ID_RY);

## Slide 10: Stall
Stall aggregator
  Inputs
    I_stall: instruction cache stall
    lw_hazard: load-use hazard
    D_stall: data cache stall
  Outputs
    stall_IF: stall IF stage
    flush_IF: bubble IF stage
    stall_ID: stall ID stage
    flush_ID: bubble ID stage
    stall_EX: stall EX stage

## Slide 11: Stall
Stall conditions
  if D_stall:
    stall IF/ID/EX
  if lw_hazard:
    stall IF/ID, flush ID
  if I_stall:
    flush IF

## Slide 13: Cache
Separate implementation of ICACHE and DCACHE
  ICACHE: read-only, 32 words, direct mapped
  DCACHE: read/write, 32 words, direct mapped, write back + write buffer

## Slide 14: Cache
Write back + write buffer
  Write buffer can hide write latency if no continuous miss
write miss
Can still read
after write miss

## Slide 15: Cache
Read preloader
  Continuous address for k read, preload next address

## Slide 16: Cache
Read preloader FSM

## Slide 17: Cache
Read preloader
  NOT used in final design
  In HW4:
    Without RP: 6164 cycles, read miss penalty: ~4 cycles
    With RP: 4172 cycles (-32.3%), read miss penalty: ~0.2 cycles
  In Final (baseline):
    Without RP: 2065 cycles
    With RP: 2074 cycles (+0.4%)

## Slide 18: Cache
Read preloader
  Why?
    In HW4, we can hide memory.v read latency
    In Final, we can’t fully hide slow_memory.v read latency
    Comparison
      Using memory.v in HW4 tb: 4182 cycles
      Using slow_memory.v in HW4 tb: 8811 cycles
    Also, ICACHE read miss rate in baseline is low (0.9%)

## Slide 19: Cache
Cache FSM

## Slide 20: Experiment: Cache Ablation Study
Ablation study
  +I: ICACHE, +D: DCACHE
  +L2I: L2 ICACHE, +L2D: L2 DCACHE

## Slide 21: Critical Path Optimization
Observation: critical path
  EX – forwarding – program counter

## Slide 22: Critical Path Optimization
Break the critical path
  Gate the forwarding unit and forwarded value by registers
  If forwarding happens, stall IF and ID, flush ID

## Slide 24: Experiment: Critical Path Optimization
Results
  No gain in terms of AT
  Clock speed can be faster, but total cycles also grows

## Slide 25: Experiment: AT
Area: 290387 (um2)
Total cycles: 2143 (baseline hasHazard)
Clock cycle: 4.08 (ns)
A x T: ~2.538 x 109

## Slide 26: Extensions

## Slide 27: Branch Prediction
Data Path

## Slide 28: Branch Prediction
FSM: 2-bit saturating counter

## Slide 29: Experiment: Branch Prediction
Comparison
  Also comparing 2-bit and 1-bit saturating counter

## Slide 30: L2 Cache
Implementation
  16~128 blocks, 128 bits/block
  Direct mapped

## Slide 31: L2 Cache
Block diagram

## Slide 32: Experiment: L2 Cache Ablation Study
Ablation study
  +I: ICACHE, +D: DCACHE
  +L2I: L2 ICACHE, +L2D: L2 DCACHE

## Slide 33: Experiment: L2 Cache Size
Different L2 cache size

## Slide 34: Experiment: L2 Cache Miss Rates
Miss rates
  Instruction cache, read miss rate

## Slide 35: Experiment: L2 Cache Miss Rates
Miss rates
  Data cache, read miss rate

## Slide 36: Experiment: L2 Cache Miss Rates
Miss rates
  Data cache, write miss rate

## Slide 37: Multiplier, Divider
Implemented Instructions
(signed)
(signed)

## Slide 38: Multiplier, Divider
Multiplier architecture

## Slide 39: Multiplier, Divider
Divider architecture

## Slide 40: Multiplier, Divider
Signed division
  Convert the dividend and divisor to positive
  Do unsigned division
  Compute the signs of the quotient and remainder
    (Quotient sign) = (Dividend sign) XOR (Divisor sign)
    (Remainder sign) = (Dividend sign)

## Slide 41: Multiplier, Divider
Comparison
  Iterative (512 cycles)
  RTL (188 cycles)

## Slide 42: Experiment: Multiplier, Divider
Comparison
  Area-speed tradeoff